Manual Instructions

Bluetooth Automatic Parking Lock

Contents 1. Packing List 2 2. Structure diagram 2 3. Technical specification 3 4. Battery Type 3 5. How to download the App 4 6. User registration 5 7. Add parking lock. 6 8. Warranty items 7 9. /Trouble shooting 7 10. Installation 7 11. Advantages 8

Manual instructions

## Packing List

| Item | Quantity |
| --- | --- |
| Automatic Parking Lock | 1 Pcs |
| Remote Control | 1 Pcs |
| Battery | Dry-4 Pcs/Recharge-1Pcs |
| Expand Screw | 3 Pcs |
| Manual | 1 Pcs |

## Structure diagram

1. Arm          2. Mounting hole of the base     3. Alarm                 4. Battery

5 Energy saving   6. Motor driven                7.Laser anti-impact device  8.Control syst

## Technical specification

| Mode | KVS-PL-BT01 |
| --- | --- |
| Dimension | 460*460*75mm |
| Net weight | 8kg |
| nominal voltage | DC6V |
| working currnet | ≤1A |
| standby current | ≤0.3MA |
| standby by time | 12months |
| control distance | 20m |
| opening time | ≤5S |
| opening height | 380mm |
| closing height | 80mm |
| working temperature | -30℃~80℃ |
| Effective bearing capacity | 2000KG |

| Battery Type | Dry Battery | Lead-acid Battery | Lithium Battery |
| --- | --- | --- | --- |
| Charging method | / | Chargeable | Chargeable |
| Battery Life | 12 months | 24 months | 5 years |
| Working Temperature | -10℃~50℃ | -10℃~50℃ | -22℃~55℃ |
| Rechage Cycle | Single use | 8 hours | 8 hours |
| Usage time | 3 to 6 months | 3 months | 8 to 12 months |

## Battery Type

## How to download the App

- IOS users please search and download “KAVASS” from App Store

- Android users please search and download  “KAVASS” from on Google Store or by link https://play.google.com/store/apps/details?id=com.ddtc.remote

## User registration

Notice: If the verification code is not received, please send it again and enter password. Then click finish.

## Add parking lock.

Notice: One parking lock service one owner.

## Warranty items

- One year warranty when the from shipping date

- The following situations are not free of charge

A. It is damaged due to transportation, operation  and management

B. It is damaged due to disassemble

C. It is damaged due to under the instruction of

D. Man-made damaged。

- Do not belong to free scope or exceed warranty period, offer to match for pay

## /Trouble shooting

When click the bottom, the parking lock can not work but it has power supply

- Check the cable connector and power supply work well or not

- Check the motor has a abnormal sound or not

- Check the arm reset or not

- Check the shape is out of shape or not

## Installation

- Installation position

The parking lock can not be impacted when vehicle come in and out. Please install it on the 1.2-1.5 meters in middle of the parking space.

- Installation place

Please install it on the flat and dry cement ground

- Installation method

A.pull the arm up by hand, open the black cover with a key and put the parking lock aside；

B.Make the fixing position of expansion bolts with mark pan according to fixing plate on the blasé plate of eparking lock, drill 3 holes( diameter 12mm and depth 80mm ) by impact drill, fix M8 expansion screw；

C.Put parking lock to the appropriate mounting position, and tighten the screw nut.

D.Connect the battery connector and parking lock, lock the cover

E. Test it in App, if it can work well then it is done.

## Advantages

- 1.long control distance

It has super long control distance. App control the arm up and down with high sensitivity and reliable operation.

- Shared among multiple people

It can be shared to family and friends as long as they get the information.

- Available to rent

Staggered parking time and resource sharing. Renting time can be chosen and the rest of time used by owner.

- //long standby time

Low cost and long standby time. Normally , the power last for one year

- Crush resistance

With mould temperature one-time die-casting molding technology, high technology surface paint treatment and Germany welding technology, the strength and integration of the parking lock has been improved. It is installed easily and has a beautiful appearance and strong structure characteristic.

- Waterproof

The advanced fully sealed design is adopted so that the parking lock can be used in indoor and outdoor,rain and snow weather

- Automatic reset and alarm system

When arm of parking lock is rising up and down, it is stopped by external force, the rocker arm will reset to the original state automatically, which can effectively prevent the damage of the parking lock itself and the car chassis.

- Power shortage indication

When there is no enough power, buzzer will alarm and power indication light in APP will turn into red.

- Emergency device//

When parking lock can not work due to the battery drains the last drop and some other problem in the system, users can operate the arm up and done manually;

- Long service life

The unique 180-degree movable retaining arm can avoid extremely strong external force damage and effectively extend the service time. The service life is up to 8 years.

- Low notice

Low noise, scientific and reasonable internal drive mechanism are better than other products in the same industry;；

- Anti-theft proof

The core parts of parking lock are all inside the shell. Shield cover can only be opened by keys.

# Text boxes

2. Choose your country and enter your phone number.

3. Enter the Picture-Code,it must be capitals.

4. Click to get the Verification Code

5. Set up your Password

1.Choose “No Account?Create One!” to create your own account

2.Enter the “Lock ID” and “Bind ID” which is on Parking Lock Box

1.Choose “Add Parking Lock” to add your own parking lock